## Slide 2: Dynamic PGO in .NET 8
Andy Ayers
Egor Bogatov

## Slide 3: .NET 8 is Fast
You probably know this already, but .NET 8 brings compelling performance improvements
  over an already fast .NET 7, which brings compelling performance improvements
    over an already fast .NET 6, which brings compelling performance improvements
      over an already fast .NET 5….
How? Literally 1000’s of improvements all across the product, big and small.
  See Performance Improvements in .NET 8 for a healthy sample
One of the “big” ones is Dynamic PGO

## Slide 4: Dynamic PGO
Automatically boosts performance of most .NET apps
  ~15% is typical
No application changes needed; all you need to do is start using .NET 8

## Slide 5: In This Talk
A behind-the-scenes look at Dynamic PGO
  Optimizations
  Instrumentation
Guidance if you’ve opted into PGO in earlier releases
Options to disable Dynamic PGO
  Which you’ll hopefully never need
Things to watch out for when benchmarking

## Slide 6: Background
PGO: Profile Guided Optimization
  A compiler technique using profile data to guide code optimization
Dynamic PGO
  Automatically gives the benefits of PGO
  Works entirely in-process, no workflow or deployment changes needed, no training or special builds required
  Leverages Tiered Compilation (introduced in .NET Core 3) to observe runtime behavior of methods by instrumenting codegen in initial tier(s) to build profiles
  These profiles guide JIT optimization of code in later tiers
  Widely used in Java (“HotSpot”) / JavaScript (“Trace JITs”)

## Slide 7: Optimizations
Guarded Devirtualization (GDV)
Profile Guided Inlining
Code Layout

## Slide 8: Guarded Devirtualization (GDV)
Many virtual and interface calls are “monomorphic” -- there is just one class observed at runtime
Even at “polymorphic” call sites there may be one predominant class
GDV will introduce tests for these specific types (the “guard”)
When the test succeeds, the JIT knows exactly which method will be called
  AKA devirtualization
  The JIT will also try and inline the method
  If the method is on a value class, the JIT will inline the unboxing stub and the method
  If the class is a boxed value type, the JIT will attempt to optimize away the box too
If the test fails, just do the normal virtual / interface call
.NET 8: GDV can handle some delegate invokes as well

## Slide 9: GDV
void RegisterUser(IUserService service, User user)
{
service.Register(user); // virtual call
}

## Slide 10: GDV
void RegisterUser(IUserService service, User user)
{
service.Register(user); // virtual call
}
void RegisterUser(IUserService service, User user)
{
CORINFO_HELP_CLASSPROFILE32(service.GetType());
service.Register(user);
}

## Slide 11: GDV
void RegisterUser(IUserService service, User user)
{
service.Register(user); // virtual call
}
void RegisterUser(IUserService service, User user)
{
CORINFO_HELP_CLASSPROFILE32(service.GetType());
service.Register(user);
}
void RegisterUser(IUserService service, User user)
{
if (service is UserServiceImpl impl)
impl.Register(user); // direct call, can be inlined
else
service.Register(); // still virtual (fallback)
}

## Slide 12: GDV Enabled Loop Cloning/Hoisting
If you have a virtual/interface/delegate call site in a loop, the guard checks within the loop may be loop invariant
  The JIT can hoist the invariant guard checks outside the loop, and clone the loop so there are two copies, one with no guard checks
This combination can (partially) deabstract some common enumeration patterns (aka “zero-cost abstraction”)
  There’s still room for improvement here…

## Slide 13: GDV Cloning / Hoisting
private static int Sum(Func<int, int> func)
{
int sum = 0;
for (int i = 0; i < 10_000; i++)
{
sum += func(i); // delegate call
}
return sum;
}
private static int Sum(Func<int, int> func)
{
int sum = 0;
if (func.Method == KnownLambda)
{
for (int i = 0; i < 10_000; i++)
{
sum += i + 1;
}
}
else
{
for (int i = 0; i < 10_000; i++)
{
sum += func(i);
}
}
return sum;
}
Tier0+Instr
  Tracks the method invoked at the delegate call site
Tier1
  Sees that just one method is invoked at the call site, and adds a GDV check
  Inlines the call on the path where the check succeeds
  Sees that the GDV check is a loop invariant, and clones the loop to create a check-free version

## Slide 14: Profile-Guided Inlining
Use profile data to ensure key methods are inlined
Relaxed thresholds for IL size and number of basic blocks
Spend less JIT time on (semi-) cold call sites

## Slide 15: Profile-Guided Inlining
bool IsPrimitiveType(Type type) =>
type == typeof(bool) ||
type == typeof(char) ||
type == typeof(sbyte) ||
type == typeof(byte) ||
type == typeof(short) ||
type == typeof(ushort) ||
type == typeof(int) ||
type == typeof(uint) ||
type == typeof(long) ||
type == typeof(ulong) ||
type == typeof(float) ||
type == typeof(double) ||
type == typeof(nint) ||
type == typeof(nuint);

## Slide 16: Profile-Guided Inlining
for (int i = 0; i < 100; i++)
{
Test<int, float>();
Thread.Sleep(16);
}
[MethodImpl(MethodImplOptions.NoInlining)]
static bool Test<T1, T2>() =>
IsPrimitiveType(typeof(T1)) &&
IsPrimitiveType(typeof(T2));
static bool IsPrimitiveType(Type type) =>
type == typeof(bool) ||
type == typeof(char) ||
type == typeof(sbyte) ||
type == typeof(byte) ||
type == typeof(short) ||
type == typeof(ushort) ||
type == typeof(int) ||
type == typeof(uint) ||
type == typeof(long) ||
type == typeof(ulong) ||
type == typeof(float) ||
type == typeof(double) ||
type == typeof(nint) ||
type == typeof(nuint);
; Assembly listing for method Program:Test[int,float]():bool ; Tier-1 compilation ; No PGO data sub rsp, 40 mov rcx, 0x11B802000B8 ; 'System.Int32' call [Program:IsPrimitiveType(System.Type):bool] test eax, eax je SHORT G_M27198_IG05 mov rcx, 0x11B80205090 ; 'System.Single' call [Program:IsPrimitiveType(System.Type):bool] nop add rsp, 40 ret G_M27198_IG05: xor eax, eax add rsp, 40 ret ; Total bytes of code 53
Inliner: too many IL bytes

## Slide 17: Profile-Guided Inlining
for (int i = 0; i < 100; i++)
{
Test<int, float>();
Thread.Sleep(16);
}
[MethodImpl(MethodImplOptions.NoInlining)]
static bool Test<T1, T2>() =>
IsPrimitiveType(typeof(T1)) &&
IsPrimitiveType(typeof(T2));
static bool IsPrimitiveType(Type type) =>
type == typeof(bool) ||
type == typeof(char) ||
type == typeof(sbyte) ||
type == typeof(byte) ||
type == typeof(short) ||
type == typeof(ushort) ||
type == typeof(int) ||
type == typeof(uint) ||
type == typeof(long) ||
type == typeof(ulong) ||
type == typeof(float) ||
type == typeof(double) ||
type == typeof(nint) ||
type == typeof(nuint);
; Assembly listing for method Program:Test[int,float]():bool ; Tier-1 compilation ; Optimized with Dynamic PGO mov eax, 1 ret ; Total bytes of code 6
Inliner:
Inline candidate has 13 foldable branches.
Inline has 28 foldable intrinsics.
Callsite has profile data: 1.0.

## Slide 18: Profile Guided Code Layout
PGO will compact the “hot code” in a method towards the start of the method.
; Tests.Sum(System.Func`2<Int32,Int32>)
push rdi
push rsi
push rbx
sub rsp,20
mov rbx,rcx
xor esi,esi
xor edi,edi
test rbx,rbx
je short M01_L01
mov rax,7FFA2D630F78
cmp [rbx+18],rax
jne short M01_L01
M01_L00:
inc edi
mov eax,edi
add esi,eax
cmp edi,2710
jl short M01_L00
jmp short M01_L03
M01_L01:
mov rax,7FFA2D630F78
cmp [rbx+18],rax
jne short M01_L04
lea eax,[rdi+1]
M01_L02:
add esi,eax
inc edi
cmp edi,2710
jl short M01_L01
M01_L03:
mov eax,esi
add rsp,20
pop rbx
pop rsi
pop rdi
ret
M01_L04:
mov edx,edi
mov rcx,[rbx+8]
call qword ptr [rbx+18]
jmp short M01_L02
private static int Sum(Func<int, int> func)
{
int sum = 0;
if (func.Method == KnownLambda)
{
for (int i = 0; i < 10_000; i++)
{
sum += i + 1;
}
}
else
{
for (int i = 0; i < 10_000; i++)
{
sum += func(i);
}
}
return sum;
}

## Slide 19: Instrumentation
How PGO gathers the data needed for optimization

## Slide 20: Instrumentation Tiers
Code versions:
R2R'd code
Tier0
Tier0 with instrumentation
Tier1 with instrumentation
Tier1 optimized with (or without) previously collected profile
Not shown here:
OSR
Tier0 with loops

## Slide 21: Instrumentation Overhead
In .NET 8 we did a lot of work to reduce overhead from instrumentation
  Dynamic PGO startup improvements in NET 8 · Issue #76969
Sparse edge profiles enabled for all methods
GDV random state now in TLS (thread-local storage)
Scalable profile counters
  JIT: scalable profile counter mode #84427
More cases where the JIT will bypass instrumentation
Enable intrinsic expansion in Tier0

## Slide 22: Impact of improvements to instrumentation on Tech Empower RPS / Latency
Tier0
Tier0 + Instr
Tier1

## Slide 23: Configuration
How to enable, disable, or update configuration settings

## Slide 24: To enable Dynamic PGO
Update to .NET 8
Dynamic PGO is enabled by default in .NET 8. Nothing else is required.
Review configuration settings to make sure you’re not disabling any of these runtime features:
  TieredCompilation
  ReadyToRun
  QuickJitForLoops
  OnStackReplacement

## Slide 25: If you’ve opted into PGO in .NET 6 or 7
Thank you for being an early adopter!
With the new tiering strategy, PGO and ReadyToRun play nicely together
You can remove the following config settings
  DOTNET_ReadyToRun=0
  DOTNET_QuickJitForLoops=1
  DOTNET_TieredPGO=1

## Slide 26: To Disable PGO
Set DOTNET_TieredPGO=0
  Or <TieredPGO>false</TieredPGO> in the project file
This will restore .NET 7’s behavior
If you disable PGO, please loop us in, so we can learn how to make it better

## Slide 27: Performance, Profiling & Benchmarking

## Slide 28
AAD Gateway
Our own benchmarks
Ryujinx
More

## Slide 29: With PGO enabled
You should see an improvement in steady-state perf
  Very short running, JIT intensive apps may not speed up
  Note even without PGO, .NET 8 can deliver impressive speedups
You may see some impact to startup
  Either longer start up times, or for a server, increased latency at startup
You may see more methods jitted overall
  Some methods will be jitted multiple times:
    Tier0, Tier0+Instrumentation, OSR, Tier1
There may be PGO specific bugs, either correctness or performance
  If you suspect a bug, try running with PGO disabled, via DOTNET_TieredPGO=0 or via the config settings
  If PGO makes things slower, contact us or file an issue

## Slide 30: PGO & Benchmarks
BenchmarkDotNet (BDN) usually does a good job of ensuring you are measuring the optimized tiers
  But if your benchmark method takes > 100ms or more, it may not
  If you are doing ad-hoc benchmarking (say via Stopwatch) you also may not see representative data
PGO may bypass certain tricks you may have used to isolate performance (eg via delegates)
  BDN itself is hardened to this.
Benchmark cases may now show unrealistic performance results when the input set is limited. PGO can infer things about those inputs (say running with just one class of data, or one string length)
  We need to keep an eye on this one… (more on next slide)

## Slide 31: … PGO & Benchmarks
Time(Input Set A) = X
Time(Input Set B) = Y
Time(50/50 Mix of A & B) = ??
Measuring specific case performance may not help you understand more general performance.
Time(50/50 Mix of A & B) will likely be greater than X or Y
From the example at left (Interface call overhead)
Time(A): 2.5ns (with PGO: ~0ns)
Time(B): 2.5ns (with PGO: ~0ns)
Time(A & B mixed): 8.0ns (with PGO: ~2ns)
With PGO this sort of thing may happen more often, in a wider variety of situations, and with greater disparity.
Advice: try and measure representative scenarios
B
A
½ A + ½ B

## Slide 32: To Recap
Dynamic PGO is enabled by default in .NET 8
It offers a broad range of performance improvements
All you need to do is update!
Let us know your experiences, good or bad!

## Slide 33: Resources
Download .NET 8 aka.ms/get-dotnet-8
.NET 8 Runtime Repo (details, issues, feedback) https://github.com/dotnet/runtime

## Slide 34: Download .NET 8
https://aka.ms/get-dotnet-8